## Slide 1
Irrigating with Harvested Water

## Slide 2
Shrubs: up to once a week - apply one gallon of water per foot of plant height
Lawns: up to once a week -
up to one inch per application
Trees: up to once a week
one inch of water under entire
Canopy (for larger trees don’t
water area within 4 feet of trunk)
Rule of thumb for watering

## Slide 3
Low
How much Water?
Low
H
H
25’ x 40’ = 1,000 ft2
Lawn
1” per week = 624 gal.
*Do we need to water lawns?
~2500 gal./month
Example #1 – lawn area
Notes: Converted woody plants in natural area into unirrigated low water use zone. Lawn used as a welcome mat, selected drought tollerant
turf that requires minimal water (could convert to a low water use zone if aesthetics acceptable). Groundcover and shrub boarder is
Established and does not require additional irrigation. Added some high water use flower pots in high visibility area near door to add interest

## Slide 4
Low
6’
3’
5’
4’
7’
2’
Plant Height (1gal/ft)
4’
5’
3’
2’
2’
Low
.5/d
.5/d
Shrubs: 43’ of plant = 43 gal.
+
Color: 1 gal./day * 7 days = 7 gal.
50 gal./week
200 gal./ month
Ornamentals
*Can we harvest & store 200 gal. per month?
Example #2
Notes: Converted woody plants in natural area into unirrigated low water use zone. Lawn used as a welcome mat, selected drought tollerant
turf that requires minimal water (could convert to a low water use zone if aesthetics acceptable). Groundcover and shrub boarder is
Established and does not require additional irrigation. Added some high water use flower pots in high visibility area near door to add interest

## Slide 5
April | 1.36
May | 0.26
June | 4.37
July | 3.42
August | 1.19
September | 1.46
October | 2.89
November | 0.93
Drought Year Rainfall (2007) Rome, GA

## Slide 6
Month | Rainfall (inches) | 624 (gal/in) | Volume (gal)
April | 1.36” | 624 | 849
May | 0.26” | 624 | 162
June | 4.37” | 624 | 2,727
July | 3.42” | 624 | 2,134
August | 1.19” | 624 | 743
September | 1.46” | 624 | 911
October | 2.89” | 624 | 1,803
November | 0.93’ | 624 | 580
Rainfall on a 20 x 50’ roof area (1,000 ft2)

## Slide 7
Condensate from Air Conditioners and Dehumidifiers
Home AC can produce over 5 gal./day

## Slide 8
Condensate Harvesting Potential | 
AC production | Example: 10 gpd
Multiply by 7 to convert to gallons per week | 70 gal. per week
Multiply by 4 to convert to gallons per month | ~280 gal. per month
Need ~7+ gpd to get 200 gpm

## Slide 9
Condensate Pumps
Pump ~25 gph with 15’ head
Cost ~ $50

## Slide 10
Rainwater & Condensate Water
Irrigation is not restricted