## Slide 1: Managing Soil Compaction in Turfgrass
Clint Waltz, Ph.D.
Extension Specialist
C&SS, University of Georgia

## Slide 2: Soil Compaction
Generally the most common problem on sports facilities and is a natural result from field use and maintenance.

## Slide 3: Soil Compaction
Reduces Pore Space
Limits Air, Water, & Nutrient Movement (Infiltration, Percolation)
Increases Water Runoff
Thins Turf
Increases Weed Growth

## Slide 4: Soil Compaction
Increases Bulk Density
Increases CO2 Levels
Reduced Turf Quality
Reduces Field Resilience
Increases Risk of Injury

## Slide 5
Soil Compaction
Soil
Texture
Water
Content
Pressure
Applied

## Slide 8: Aeration
The process of improving soil air exchange enhancing water and nutrient penetration into the soil, and reducing soil compaction.

## Slide 9: Factors Influencing Aeration
Frequency & Intensity of Field Use
Soil Texture & Structure
Soil Moisture at the Time of Use
Turfgrass Cover
Turfgrass Species/Cultivar

## Slide 10
Soil Properties
Physical
Chemical
Biological
Climate
Temperature
Moisture
Light
Wind
Gases
Management
Mowing
Fertilization
Irrigation
Pesticides

## Slide 11: Benefits of Aerification
Relieve soil compaction
Aid in thatch control
Improve soil air exchange
Enhance water & nutrient penetration
Disrupt undesired soil layer
Aid in modifying soil with topdressing
Enhance water & nutrient uptake

## Slide 12: Benefits of Aerification
Increase pesticide effectiveness
Reduce runoff & puddling
Increase soil temperature
Reduce effects of localized dry spots
Reduce surface hardness
Stimulate new growth
Improve heat & drought tolerance

## Slide 13: Drawbacks to Aerification
Turf injury increasing potential for turf loss during stress
Disruption of the turf surface
Increased insect problems
Increase desiccation and/or injury
Reduced soil strength
Creation of a localized soil compaction zone
Greater potential for water loss

## Slide 14: Principles of Aerification
Step One:
  Identify Problem Correctly
Step Two:
  Determine most effective means of alleviating problem

## Slide 17: Aeration Methods
Core
Solid Tine
Deep Time
Deep Drilling
Grooving
Slicing
Spiking
Sub-Aerification
High pressure water/air injection

## Slide 18: Penetration Factors
Soil Type
Soil Moisture
Tine Diameter
Weight & Power of Aerator

## Slide 19: Scheduling Factors
Considerations
Location
Species/Cultivar
Intensity of Use
Timing - prior to or during early season root growth

## Slide 20: Timing Factors
Stage of plant growth
Effect on playing surface
Scheduling
Remember:
The larger the space (core hole) the longer the growing period needed for recovery

## Slide 21: Scheduling Factors
Caution:
Avoid coring if possible when grasses are dormant because this may encourage cool-season weed competition.
Remember:
Repeated aeration to the same depth can cause a “Cultivation Pan”.

## Slide 22: Cultivation Time Frames
Cool-season
Mid Spring
To
Late Fall
Warm-season
Early Spring
To
Mid Summer

## Slide 23: Core Aeration
One of the most important management practices for maintaining high quality playing fields, and often one of the least appreciated or used practices.

## Slide 24: Tine Types
Type Action
Hollow Removes
Open/Spoon Divots
Solid Lifts, Cracks, & Shatters

## Slide 26: Core Surface Area Calculations
5 inch
5 inch
1 inch
Tine Diameter = 1 inch
Tine Radius = 1 in. / 2 = 0.5 inch
Area of Spacing = 5 in x 5 in = 25 inch2
Area of Core = r2
Area of Core = 3.141*(0.5 in)2
Area of Core = 3.141*0.25 in2
Area of Core = 0.785 in2
Surface Area Affected = Area of Core/Area of Spacing
Surface Area Affected = 0.785 in2 / 25 in2
Surface Area Affected = 0.031 in2 or 3.1%

## Slide 27: Tine Spacing: 5x5 inches
Tine Size Diameter (in.) | Spacing (in.) | # of Holes / sq. ft. | Surface Area Impacted / tine (sq. in.) | Surface Area Impacted (%) | # of Passes to remove 20%
1/2 | 5x5 | 5.76 | 0.196 | 0.79% | 25.5
3/4 | 5x5 | 5.76 | 0.442 | 1.77% | 11.3
1 | 5x5 | 5.76 | 0.785 | 3.14% | 6.4

## Slide 28: Tine Spacing: 5/8 inch
Tine Size Diameter (in.) | Spacing (in.) | # of Holes / sq. ft. | Surface Area Impacted / tine (sq. in.) | Surface Area Impacted (%) | # of Passes to remove 20%
5/8 | 4x4 | 9 | 0.307 | 1.92% | 10.4
5/8 | 5x5 | 5.76 | 0.307 | 1.23% | 16.3
5/8 | 6x6 | 4 | 0.307 | 0.85% | 23.5

## Slide 31: Best Practices
6 in. Spacing with 1 in. Tines
3 Passes in Differing Directions
Twice a Year (Spring & Fall)
Water 12 to 24 hours Before
Removing Cores
Top-dress with Sand

## Slide 32: Topdressing

## Slide 33: Topdressing: Sand
Keep pores open
Helps with thatch

## Slide 34: Slicing / Spiking

## Slide 35: Slicing / Spiking
Forgotten practice
Often as possible
Opens the soil

## Slide 36: High Pressure Injection

## Slide 37: High Pressure Injection
Minimal surface disruption
Often as possible
Opens the soil

## Slide 38: Important Dates in 2004
North Georgia Field Day
    Gainesville - May 19, 2004
Turf Field Day
    Griffin – August 12, 2004
Turfgrass Institute
    Duluth – December 7 - 8

## Slide 39: Thank You
Visit
WWW.Georgiaturf.com
and
WWW.Turfgrasswater.com

## Slide 40
Renovation
and Management of Sports Turf Fields

## Slide 41
Challenge of Sports Turf Managers
Provide a field with beautiful green grass that is almost always playable and safe under heavy field usage (abuse)

## Slide 42
Budget plays a vital role in the degree of success and determines one’s expectations

## Slide 43
Sports Turf Field Success Formula
Water management
Vigorous
maintenance
Limited Usage
Proper design and construction

## Slide 44
Regulating Field Use

## Slide 45: Usage Maxims (200-400-600 Rule)
Generally advise that a field not be used in excess of 200 hours per year in order to sustain good field conditions
Under some circumstances, fields have successfully handled between 400 to 600 hours of use per year with good field conditions
Beyond 600 hours, you are expecting miracles and will be playing on dirt
Notes: After a few years, some general guidelines I use related to field use (and overuse). I often get the question . . . “how much can my field be used”.

## Slide 46
Overseeding WEAKENS the permanent turfgrass and will delay its green-up and growth in the spring

## Slide 47
Overseeding Turfgrass Selection
        Annual Ryegrass
        Intermediate Ryegrass
        Perennial Ryegrass

## Slide 48
Renovation ?

## Slide 49
Is this field safe?
Is your field safe?
Notes: Good slide of field worn to the dirt.