## Slide 1: Microbiological Examination of Water
January 17, 2007
Dr. Paul F. Vendrell

## Slide 2: Agenda
Water-borne diseases
Pathogen indicators
  Coliform
  Streptococcus
  Enterococcus
Enumeration Methods
  Membrane filter
  Multiple tube fermentation
Surface Water Standards
How much water can wild birds contaminate?
Survival and Transport

## Slide 3: Water borne pathogens
Bacteria
Virus
Protozoa
Helmiths
Spirochete
Rickettsia
Algae
1991 Cholera Epidemic 1,000,000 cases/10,000 deaths

## Slide 4: Bacteria
Enteritis, diarrhea, and dysentery
  Campylobacter
  Cholera
  E. coli 0157:H
  Salmonella
  Shigella
Enteric fever
  Typhoid
  Paratyphoid
Paralysis
  Botulism

## Slide 5: Bacteria…….continued
Eye, ear, and skin infections
  Miscellaneous bacteria
Urinary tract infections
  E. coli
  Others

## Slide 6: Viruses
Enteritis, diarrhea, and dysentery
  Rotavirus
  Norwalk
Flu like (liver damage)
  Hepatitis A
  Hepatitis E
Paralysis
  Polio

## Slide 7: Protozoa
Giardia
Cryptosporidia
Amoeba

## Slide 8: Helmith
Round worm
Tape worm
Hook worm
Whip worm

## Slide 9: Others…..
Algae
  Mycrocystis
  Dinoflaggelates
Fungi
Water-related diseases
  Malaria
  Schistosomiasis
  Yellow fever
  Dengue fever

## Slide 10: Problems
Numerous water borne pathogens
Individual pathogen numbers may be too low to detect in a reasonable sized water sample
Isolation and detection of some pathogens can take several days, weeks, or months
Absence of one particular pathogen does not rule out the presence of another

## Slide 11: Indicator Organism Concept
Correlated to the presence of pathogens
Population large enough to isolate in small water samples (100 mL)
Rapid
Inexpensive
Safety, not culturing pathogens

## Slide 12: Coliform Group (total coliform)
Enterobacteriaceae
  Facultative anaerobe
  Gram negative
  Non-spore forming
  Rod shaped
  Ferment lactose
  Produce gas and acid within 48 h @ 35 C
Coliform genera
  Enterobacter
  Klebsiella
  Citrobacter
  Escherichia

## Slide 13: Coliform Group
Total coliform
Fecal coliform
  All total coliform criteria
  Grows at 44.5 C
Escherichia coli
  Individual species
  Enzyme specific
total coliform
fecal coliform
E. coli

## Slide 14: Streptococcus and Enterococcus
Fecal Strep
  S. faecalis
  S. faecium
  S. avium
  S. bovis
  S. equinus
  S. gallinarum
Enterococcus
Fecal Streps that survive in 6.5% sodium chloride
  S. faecalis
  S. faecium
  S. avium
  S. gallinarum

## Slide 15: Membrane Filter Methods
Filter water through a 0.45 μM membrane filter
Place membrane on selective media
Incubate
  35 C total coliform
  44.5 C fecal coliform
Count colonies

## Slide 16: Multiple Tube Fermentation Methods
Serial dilution to extinction
Inoculate multiple tubes (5 or 10) of media with across the increasing series of dilutions
Incubate
  35 C or
  44.5 C
Count positive growth tubes
Use Most-Probable-Number (MPN) table to estimate density

## Slide 17: Enzyme Substrate or Chromogenic Substrate Method
Used with the Presence-Absence, the Multiple Tube Methods, or Quanti-TraysTM
Total coliform have the enzyme
  β-D-galactosidase which hydrolyses
  ortho-nitrophenyl- β-D-galactopyranoside (ONPG)
  Yellow when hydrolyzed
E. coli has the enzyme
  β-glucuronidase which hydrolyses
  4-methylumbelliferyl-β-glucuronide (MUG)
  Fluoresces when hydrolyzed

## Slide 18
ONPG-Total Coliform
MUG- E. coli

## Slide 19: Georgia EPD Fecal Coliform Standard for Water Contact Activities
Geometric mean (GM)
  GM= (Y1 * Y2 * Y3 * Y4)1/4
  At least 4 samples
  Over a 30-day period
  At least 24 hours apart

## Slide 20: Fishing and Drinking--Fecal Coliform Standards…cont.
May thru October
  GM not to exceed 200 MPN/100-ml
  No individual samples exceeding 4,000 MPN/100-ml
November thru April
  GM not exceeding 1,000 MPN/100-ml
  No individual sample exceeding 4,000 MPN/100-ml

## Slide 21: EPAs E. coli Criteria
Illness Rate/1000 | Geometric Mean/100mL | Single Sample/100mL
8 | 126 | 235
9 | 206 | 300
10 | 206 | 383
11 | 263 | 490
12 | 336 | 626
13 | 429 | 799
14 | 548 | 1021

## Slide 22: Look-out for that DIRTY-BIRD!!!
Gulls
Geese

## Slide 23: Worse Case Gull and Goose Dropping
 | Dropping Weight (wet-g) | Fecal Coliform (CFU/wet-g) | Fecal Coliform Load (CFU)
Ring-Billed Gull | o.54 | 1.52 x 109 | 8.21 x 108
Canada Goose | 9.98 | 2.42 x 107 | 2.41 x 108
From: Alderisio, K. A. and N. DeLuca. 1999. Seasonal enumeration of fecal coliform bacteria from feces of ring-billed gulls (Larus delawarensis) and Canada Geese (Branta canadesis). App. Environ. Microbiology. p. 5628-5630.

## Slide 24: How much water could one Gull dropping increase to 200 MPN/100 ml?
Gull
  8.21 x 108 Fecal Coliform/dropping
  4.105 x 105 liters
  1.084 x 105 gallons
  3.99 acre inches
  1.45 x 104 feet3

## Slide 25: How much water could one Goose dropping increase to 200 MPN/100 ml?
Goose
  2.41 x 108 Fecal Coliform/defecation
  1.205 x 105 liters
  3.183 x 104 gallons
  1.17 acre inches

## Slide 26: 10 geese defecating during a day of feeding 123 acre feet @ 200/100mL

## Slide 27: 100 gulls defecating one time 33 acre feet @ 200/100 mL

## Slide 28: Factors that determine the fecal coliform concentration in water
Transport
Survival/Die-off
Source

## Slide 29: Factors Affecting Bacterial Survival/Die-off
Drying
Temperature
pH
uV Radiation
Competition
Predation
Toxic substance

## Slide 30: Factors Effecting Transport
Precipitation
Slope
Runoff
Soil type
Surface features
Deposition proximity to water
Relationship with sediment