## Slide 1: Prioritizing Sports Turf Practices
Clint Waltz, Ph.D.
Extension Turfgrass Specialist
The University of Georgia

## Slide 2: Sports Fields

## Slide 3: Designing, Constructing, & Maintaining Bermudagrass Sports Fields
For Sale Publication - Order information
www.GeorgiaTurf.com
Ag. Business Office Room 215, Conner Hall Athens, GA 30602 (706) 542-8999 or 8575 www.caes.uga.edu/publications/for_sale.html

## Slide 4: Design & Construction Considerations

## Slide 5: Sports Turf Field Success Formula
Water management
Vigorous
maintenance
Limited Usage
Proper design and construction

## Slide 6: Three Most Important Factors!
DRAINAGE
DRAINAGE
DRAINAGE

## Slide 7
160 - feet
12 to 18-inch crown
drainage tile

## Slide 8
“Turtle-Back“
Drainage Design
center area flat
(no slope)
“Hip Roof”
Drainage Design
To
Outlet
18-inch center crown
Tile Line
1 to 2% slope
1 to 2% slope
Tile Line
(hash mark)
Tile Line

## Slide 9
drainage tile line
warning track
1 to 2% grade
infield
turf
drainage tile line
8 to 12" fall
8 to 12" fall
10 to 12" fall
10 to 12" fall
6 to 8" fall
"hip"
area
"hip"
area
6 to 8" fall
6 to 8" fall
surface catch basins (drains)
drainage tile line
1 to 2% grade
skinned area
outfield turf
90 ft
90 ft

## Slide 10: Sand Rootzones: USGA
Turfgrass
12” Sand
Rootzone
4” Diameter Round Drain in Gravel Trench
Subsoil
Turfgrass
12” Rootzone Mix
Subsoil
4” Diameter Round Drain in Gravel Trench
4” Pea Gravel Layer

## Slide 11: Sand Rootzones: Sand Cap
Turfgrass
4” Sand
Rootzone
4” Diameter Round Drain in Gravel Trench
Subsoil
Turfgrass
4” Sand
Rootzone
Subsoil

## Slide 12: Challenge of Sports Turf Managers
Provide a field with beautiful green grass that is almost always playable and safe under heavy field usage (abuse)

## Slide 13: Is this field safe?
Notes: Good slide of field worn to the dirt.

## Slide 14
Budget plays a vital role in the degree of success and determines one’s expectations

## Slide 15: Sports Turf Field Success Formula
Water management
Vigorous
maintenance
Limited Usage
Proper design and construction

## Slide 16
Regulating Field Use

## Slide 17: Wear: Usage Maxims (200 – 400 – 600 Rule)
200 – to sustain good field conditions use should not exceed 200 hours / year
400 – some fields can handled between 400 to 600 hours of use / year
600 - 600 hours / year is extreme and poor conditions can be expected

## Slide 18: Bermudagrass

## Slide 19: Bermudagrass Cultivars
Vegetative
‘Tifway’ / 419, ‘TifSport’ & ‘Tifton 10’
  Shade – ‘Celebration’
Certified grass
  encourage the consumer
Putting green cultivars
  ‘Tifdwarf’, ‘TifEagle’, ‘Mini Verde’

## Slide 20: Bermudagrass Cultivars
Seeded
‘Princess 77’, ‘Riviera’, ‘Sahara’
Availability
Seeding rate – 1 lb / 1000 ft2
Cost
  $30 / lb for 1000 ft2
  $75 / pallet for 500 ft2 pallet = $150 / 1000 ft2

## Slide 21: Turfgrass Cultivars
New or Old
Supply
Find local grower
  costs – drop charges, fuel sur-charge
www.GeorgiaTurf.com
  Turfgrasses link

## Slide 22: 2006 Turfgrass Costs
 | On-the-farm |  |  |  | Delivered to Atlanta* |  | 
Turfgrasses | 2005 | 2006 | Change |  | 2005 | 2006 | Change
 | --- Cents / ft2 --- |  | % |  | --- Cents / ft2 --- |  | %
Bermudagrass | 11.4 | 12.4 | 8.8 |  | 15.4 | 16.3 | 5.8
Zoysiagrass | 24.4 | 21.4 | -12.3 |  | 30.6 | 32.4 | 5.9
Centipedegrass | 15.1 | 14.8 | 2.0 |  | 19.8 | 20.3 | 2.5
Tall Fescue | 18.0 | 20.6 | 14.4 |  | 23.1 | 25.0 | 8.2
St. Augustinegrass | 21.9 | 24.9 | 13.7 |  | 28.0 | 31.0 | 10.7
* Delivered price includes freight and pallets.

## Slide 23: 2006 Bermuda Supply
* Projected supply for the first 5 months of the calendar year.

## Slide 24: Bermudagrass Cultivar Water Usage
a
ab
cd
c
d
a
a
a
a
ab
b
a
Baldwin et al., 2006

## Slide 25: Bermudagrass Cultivar Water Usage
a
a
bc
bc
c
ab
a
a
ab
ab
b
ab
Baldwin et al., 2006

## Slide 26: Bermudagrass Cultivar Water Usage
a
a
b
a
a
a
a
a
b
ab
a
ab
Baldwin et al., 2006

## Slide 27: Bermudagrass Cultivar Water Usage
a
ab
b
a
a
a
ab
a
b
a
b
a
Baldwin et al., 2006

## Slide 28: Bermudagrass Cultivar Water Usage
c
b
ab
a
Baldwin et al., 2006

## Slide 29: Timing N Fertilization
Warm-season Grasses
Soil Temperatures
  Active root growth
  65° F
  Consistently – multiple days
  4-inch depth
  www.GeorgiaWeather.net
  Combination products

## Slide 30: Bermuda Fertilization
Common concerns
  Don’t fertilize late in the season!
    succulent turf
    winter injury
    delay spring green-up
    susceptible to fall diseases

## Slide 31: Bermuda Fertilization
New Thoughts
Fertilization
  balanced ratios of N & K
  late season applications do not affect freeze tolerance
Caveat
  soluble N at 0.5 to 1.0 lb N / 1000 ft2
  2 to 4 weeks prior to hard frost
  not in areas with historical SDS

## Slide 32: Bermuda Fertilization
 | Turf Color |  | 
N Rate | (1-9, 6=acceptable) |  | GH Regrowth
(lbs N / 1000 ft2) | Oct. 16 | Oct. 23 | (%)
NTC | 4.4 b | 4.3 c | 28.6 a
2.5 | 5.3 a | 4.9 b | 24.7 a
5.0 | 5.3 a | 6.3 a | 26.1 a
N applied Aug. 30 & Sept. 27 in Blacksburg, VA. (Ervin et al., 2004)

## Slide 33: Bermuda Fertilization
N applied 2nd week Oct. in Starkville, MS. (Ervin et al., 2004)
 |  | Turf Color |  |  |  | Rhizome TNC | 
N Rate |  | (1-9, 6=acceptable) |  |  |  | (g/kg) | 
(lbs N / 1000 ft2) |  | Oct. 17 | Oct. 31 | Apr.6 |  | Dec. | Mar
NTC |  | 5.3 | 5.8 | 6.3 |  | 14.2 | 14.6
1.0 |  | 6.2* | 7.1* | 6.9* |  | 14.4 | 14.2
2.0 |  | 6.3* | 7.3* | 6.8* |  | 13.2 | 13.6

## Slide 34: Construction Considerations

## Slide 35: Most Important Factors!
DRAINAGE
DRAINAGE
DRAINAGE

## Slide 36: Soil Compaction & Wear

## Slide 37: Soil Compaction
Generally the most common problem on sports facilities and is a natural result from field use and maintenance.

## Slide 38: How do fields become hard?
Traffic
Wear - removes biomass that provides cushion and impact absorption
Compaction - packing of soil particles into a given volume, resulting in a denser soil with decreased pore space

## Slide 39: Traffic Types
Equipment Traffic
  Maintenance
  Construction

## Slide 40: Traffic Types
Foot Traffic
  Maintenance
  Athletic event
  Practice
  Band

## Slide 41: Wear: Mowing Height
Proper Mowing Height - bermudagrass
  Raising from ½- to 1-inch
    improved impact adsorption
  > 1½-inch
    shoot density declines
    blades more prone to wear
    fewer plant to recover

## Slide 42: Aeration
The process of improving soil air exchange enhancing water and nutrient penetration into the soil, and reducing soil compaction.

## Slide 43: Core Cultivation
One of the most important management practices for maintaining high quality playing fields, and often one of the least appreciated or used practices.
If used correctly, core cultivation truly relieves soil compaction, other cultivation practices are generally for thatch control and establishment.

## Slide 44: Principles of Aerification
Step One:
  Identify Problem Correctly
Step Two:
  Determine most effective means of alleviating problem

## Slide 45: Soil Compaction: Locations
Player benches
B/t hash-marks
Sidelines
On-deck circles
Path to “Home”
Goal mouths
Common worn areas of football fields

## Slide 46: Aeration Methods
Core
Solid Tine
Deep Time
Deep Drilling
Grooving
Slicing
Continuous Grooving

## Slide 47: Tine Size & Surface Area
Tine Size (in) | Spacing (in - sp) | Holes / ft2 | SA / Tine (in2) | SA Affected (%)
1/4 | 1.25 | 100 | 0.049 | 3.41
1/4 | 2.5 | 25 | 0.049 | 0.85
1/2 | 1.25 | 100 | 0.196 | 13.64
1/2 | 2.5 | 25 | 0.196 | 3.41
5/8 | 2.5 | 25 | 3.07 | 5.33
Oatis, 2003

## Slide 48: Mowing, Fert., & Coring
Michigan State Univ., 2002
Mow | Fert. | Coring | % Turfgrass Cover |  |  | Cost
(x/wk) | (lbs. N) | (x/yr) | Oct. 1 | Oct. 15 | Nov. 16 | (season)
1 | 5 | 0 | 75 | 78 | 33 | $2,716
2 | 5 | 2 | 87 | 83 | 45 | $5,207
1 | 7 | 0 | 80 | 85 | 37 | $2,886
2 | 7 | 2 | 88 | 88 | 50 | $5,377

## Slide 49: Aeration Methods
Spiking
Sub-Aerification
High pressure water/air injection
Aerify & Backfill in one process

## Slide 50: Slicing / Spiking
Forgotten practice
Often as possible
Opens the soil
  Infiltration
  Gas exchange
  stimulates growth
  soil-to-seed contact

## Slide 51: Important Dates in 2006
Southeastern Turf Conference – May 1 & 2
N. Ga. Turfgrass Field Day – May 24
UGA Turfgrass Field Day – August 15
GSPA Field Day – November 1
Turfgrass Institute – December 5 & 6

## Slide 52: Thank You
Visit
www.Georgiaturf.com
and
www.Turfgrasswater.com

## Slide 53: Factors Influencing Aeration
Frequency & Intensity of Field Use
Soil Texture & Structure
Soil Moisture at the Time of Use
Turfgrass Cover
Turfgrass Species/Cultivar

## Slide 54: Benefits of Aerification
Relieve soil compaction
Aid in thatch control
Improve soil air exchange
Enhance water & nutrient penetration
Disrupt undesired soil layer
Aid in modifying soil with topdressing
Enhance water & nutrient uptake

## Slide 55: Benefits of Aerification
Increase pesticide effectiveness
Reduce runoff & puddling
Increase soil temperature
Reduce effects of localized dry spots
Reduce surface hardness
Stimulate new growth
Improve heat & drought tolerance

## Slide 56: Soil Compaction: Soil Pores
Well sorted
Loose packed
Well graded
Loose packed
Well sorted
Tight packed

## Slide 57: Soil Compaction: Components
Soil Compaction
Soil Texture (%)
Sand (2.0 – 0.05 mm)
Silt (0.05 – 0.002 mm)
Clay (<0.002 mm)
Water Content
allows soil particles to move easier while pressing together
Pressure Applied
Foot traffic
Equipment traffic

## Slide 58: Soil Texture: Relative BD
Textural Class | Bulk Density (g/cm-3) | 
Sands or Compacted Clay | 1.4 – 1.8 | More Compacted
Loam | 1.2 – 1.6 | 
Loose silt loams or clay | 1.0 – 1.4 | 
Organic soils | 0.2 – 1.0 | Less Compacted
McCarty, 2001

## Slide 59: Soil Compaction: Soil Pores
Pore Class | Diameter (mm) | Characteristics & Function
Macropores | +5 – 0.08 | Water drains by gravity Transmits air Large enough for plant roots
Micropores | 0.08 - <0.0001 | Retain water after drainage Water moves by capillary action Root hairs can penetrate Too small for large molecules & microorganisms

## Slide 60: Soil Compaction: Direct
Increases soil bulk Density
  Reduces Pore Space
  Altered pore size distribution
Limits Air, Water, & Nutrient Movement
  Reduces infiltration
  Reduces percolation
Increases CO2 Levels
Standing water due to compaction

## Slide 61: Soil Compaction: Indirect
Thins Turf
  Reduced Turf Quality
Increases Water Runoff
Reduces Field Resilience
  Increases Risk of Injury
Increases Weed Growth

## Slide 62: Soil Compaction: Measurement
Bulk Density
  Laboratory
  Destructive
  g cm-3
Surface Hardness
  Clegg Impact Soil Tester
  deceleration
  gmax = 70 - 120
Clegg Impact Soil Tester

## Slide 63: Soil Compaction: Measurement
Water Infiltration
  Double ring infiltrometer
  in / hr
Soil Strength
  penetrometer
  psi
  scaled (Turf Tec)
Turf Tec Penetrometer

## Slide 64: Gas Movement
Gas exchange - occurs through diffusion and its efficiency depends on a continuous network of macropores from the surface and down through-out the rooting depth.
Oxygen diffusion – 10,000 times slower through water than through air
Compacted soil – a soil devoid of macropores will reduce the oxygen diffusion rate

## Slide 65: Drawbacks to Aerification
Turf injury increasing potential for turf loss during stress
Disruption of the turf surface
Increase desiccation and/or injury
Reduced soil strength
Creation of a localized soil compaction zone
Greater potential for water loss

## Slide 66: High Pressure Injection
Minimal surface disruption
Often as possible
Opens the soil
Original HPI: Hydroject

## Slide 67: Penetration Factors
Soil Type
Soil Moisture
Tine Diameter
Weight & Power of Aerator

## Slide 68: Scheduling Factors
Considerations
Location
Species/Cultivar
Intensity of Use
Timing - prior to or during early season root growth

## Slide 69: Timing Factors
Stage of plant growth
Effect on playing surface
Scheduling
Remember:
The larger the space (core hole) the longer the growing period needed for recovery

## Slide 70: Scheduling Factors
Caution:
Avoid coring if possible when grasses are dormant because this may encourage cool-season weed competition.
Remember:
Repeated aeration to the same depth can cause a “Cultivation Pan”.

## Slide 71: Cultivation Time Frames
Cool-season
Mid Spring
To
Late Fall
Warm-season
Early Spring
To
Mid Summer

## Slide 72: Tine Types
Type Action
Hollow Removes
Open/Spoon Divots
Solid Lifts, Cracks, & Shatters

## Slide 73: Best Practices
Twice a Year - minimum
  late-spring
  early-fall
Water 12 to 24 hours Before
Remove Cores
Topdress

## Slide 74: Usage Maxims (200-400-600 Rule)
Generally advise that a field not be used in excess of 200 hours per year in order to sustain good field conditions
Under some circumstances, fields have successfully handled between 400 to 600 hours of use per year with good field conditions
Beyond 600 hours, you are expecting miracles and will be playing on dirt
Notes: After a few years, some general guidelines I use related to field use (and overuse). I often get the question . . . “how much can my field be used”.

## Slide 75: Topdressing

## Slide 76: Topdressing: Sand
Keep pores open
Helps with thatch

## Slide 77
Soil Properties
Physical
Chemical
Biological
Climate
Temperature
Moisture
Light
Wind
Gases
Management
Mowing
Fertilization
Irrigation
Pesticides

## Slide 80: Slicing / Spiking

## Slide 81: High Pressure Injection

## Slide 83: Core Surface Area Calculations
5 inch
5 inch
1 inch
Tine Diameter = 1 inch
Tine Radius = 1 in. / 2 = 0.5 inch
Area of Spacing = 5 in x 5 in = 25 inch2
Area of Core = r2
Area of Core = 3.141*(0.5 in)2
Area of Core = 3.141*0.25 in2
Area of Core = 0.785 in2
Surface Area Affected = Area of Core/Area of Spacing
Surface Area Affected = 0.785 in2 / 25 in2
Surface Area Affected = 0.031 in2 or 3.1%

## Slide 84: Tine Spacing: 5x5 inches
Tine Size Diameter (in.) | Spacing (in.) | # of Holes / sq. ft. | Surface Area Impacted / tine (sq. in.) | Surface Area Impacted (%) | # of Passes to remove 20%
1/2 | 5x5 | 5.76 | 0.196 | 0.79% | 25.5
3/4 | 5x5 | 5.76 | 0.442 | 1.77% | 11.3
1 | 5x5 | 5.76 | 0.785 | 3.14% | 6.4

## Slide 85: Tine Spacing: 5/8 inch
Tine Size Diameter (in.) | Spacing (in.) | # of Holes / sq. ft. | Surface Area Impacted / tine (sq. in.) | Surface Area Impacted (%) | # of Passes to remove 20%
5/8 | 4x4 | 9 | 0.307 | 1.92% | 10.4
5/8 | 5x5 | 5.76 | 0.307 | 1.23% | 16.3
5/8 | 6x6 | 4 | 0.307 | 0.85% | 23.5

## Slide 86
Renovation ?

## Slide 87: Cultural Practices
Thatch
  Spongy collection of living & dead material
  Not all bad
    natural cushion (endure wear & tear)
    retains moisture
    insulates soil from temp. extremes
Thatch
Sod layer
Rootzone
Kentucky Bluegrass

## Slide 88: Green-up Problems
Possible Causes
  Thatch
    Likely above 2” HOC
    Excessive nitrogen
    Excessive irrigation
    Increase disease incidences
Thatch
Sod layer
Rootzone
Kentucky Bluegrass

## Slide 89: Advantages of Thatch
Approx. ½ inch
  Adds resiliency to the turf
  Increases wear tolerance
  Increases impact absorption

## Slide 90: Disadvantages of Thatch
Greater than ½ inch
  Harbors insects & disease
  Limits root penetration
  Reduces water infiltration
  Limits seed establishment
  Affects field performance

## Slide 91: Thatching of Common Grasses
Thatching Tendency | Turfgrass
Moderate to Heavy | Bermudagrass Zoysiagrass Kentucky Bluegrass
Low to Moderate | Buffalograss
 | Creeping Red Fescue
Low (or nonthatching) | Tall Fescue Perennial Ryegrass
Puhalla et al., 1999

## Slide 92: Thatch Management
Reduction
  Actively growing
  Removal
    Aerification
    Vertical mowing
    Topdressing

## Slide 93: Cultural Practices
Aerification
  When - turf actively growing
  Remove thatch and organic layer
  Equipment -
    solid vs. hollow tines
    rental

## Slide 94: Core Aerification
Common Questions
  Solid or Hollow?
    Hollow increased macropores
  Duration?
    3 weeks

## Slide 95: Core Aerification
3 times per year
  Spring Green-up
  Early Summer
  After Playing Season

## Slide 96: Topdressing
Reasons
  Thatch management
  Surface leveling
  Soil amendment
  Improve drainage
  Assist in overseeding

## Slide 97: Topdressing
Procedures
  Light & frequent
    1/16 to 3/8”
  Reaching soil surface
    mow turf low
    broom or rub-in

## Slide 98: Topdressing
Material
  Similar to existing
    Chemically
    Physically
  Prevent layering

## Slide 99
Overseeding WEAKENS the permanent turfgrass and will delay its green-up and growth in the spring

## Slide 100: Overseeding Transition
Transition early
  Improved bermudagrass cover
  Consecutive years
  Herbicide aids
    sulfonylureas
    pronamide - restricted
Gelernter and Stowell, 2005
Revolver – 17 fl oz / A

## Slide 101
Overseeding Turfgrass Selection
        Annual Ryegrass
        Intermediate Ryegrass
        Perennial Ryegrass

## Slide 102: Bermudagrass Water Usage
Baldwin et al., 2006
a
a
b
c
c
b

## Slide 103: Bermudagrass Water Usage
Baldwin et al., 2006
b
b
ab
a
b
ab

## Slide 104: Bermudagrass Water Usage
a
cd
a
d
ab
bc
Baldwin et al., 2006