## Slide 1
2008 Rain Harvest Workshop
Frank Henning
UGA Watershed Extension Agent

## Slide 2
Workshop Support
Notes: Thanks to USDA CSREES Water Quality Program

## Slide 3: Georgia’s Water
9.5 million people depend on a clean water supply.
The population is increasing by more than 2.2 % a year making GA the 5th fastest growing state in the nation.
http://drought.unl.edu/gallery/2007/Georgia/LakeHartwell2.htm
© 2006 National Drought Mitigation Center

## Slide 4
Georgia’s Growth & Water Use
1950 - 2000
- GA Water Use increased 20% between 1990 – 2000 (EPD, 2007)
- 16% increase in population projected for 2000 – 2010 (Bachel, 2003)

## Slide 5
1/2 population in
12 urban counties
2/3 population
in 40 counties
Urban Areas

## Slide 6: Water Restrictions
Georgia one of the fastest growing states
Demand for water is increasing
Water is not unlimited
Lack of water can harm
-wildlife
-landscapes
-business

## Slide 8
reduce erosion
increases infiltration
Environmental Benefits
reduce water use

## Slide 9
Rainwater & Condensate Water
Irrigation is not restricted (ban proof)
Large quantities can be harvested
- May be enough to meet landscape needs

## Slide 10
Irrigating with Harvested Water
Frank Henning
UGA Watershed Extension Agent

## Slide 11
?
1. How much water is needed for irrigation?
2. How much water can be harvested?
?
3.How much water can be stored?
?
needs
supply
storage

## Slide 12
Shrubs:
-Simple - apply one gallon of water per foot of plant height (daily, weekly, or monthly)
-Scientific – ET or soil moisture
Lawns
up to once a week - one inch per
application
Trees
up to once a week, one inch of water
under entire canopy
Rules of thumb for irrigation

## Slide 13
Low
Area based
water use
Low
H
H
25’ x 40’ = 1,000 ft2
Lawn
1” per week = 624 gal.
Do we need to water lawns?
~2500 gal./month
Notes: Even a small lawn that is only 1,000 square feet may need nearly 2,500 gallons of irrigation each month. Are we interested in storing 2,500 gallons of water for every 1,000 square feet of lawn area. Will turf survive without supplemental irrigation? Can we live with dormant turf?

## Slide 14
Drought Tolerance of Turfgrasses
Hybrid bermudagrass
Zoysiagrass
St. Augustinegrass
Centipedegrass
Tall Fescue
Most
Least
Notes: 14
As you can see not all turfgrass species are created equally. In Georgia we are lucky to be in a transition area where many different species of turf can be grown. Please consider choosing a turfgrass based on its drought tolerance.

## Slide 15
6’
3’
6’
4’
7’
Water use based on
Plant Height
4’
7’
3’
7’
3’
50’ of plant = 50 gal.
50 gal./week
~200 gal./ month
Ornamentals
*Can we harvest & store 200 gal. per month?
Notes: If you add the height of all the woody plants in this landscape that need irrigation the total sum is 50 feet. In your landscape you may have drought resistant plants that only need to be watered every other week, once a month or not at all. However, if we use our rule of thumb on this landscape and provide 1 gallon of water per foot of plant height we would apply 50 gallons of water per week, or 200 gallons per month. Can we store 200 gallons of water.

## Slide 16
Plant | Plant height | Irrigation events / month | *Total monthly Irrigation
Ex) Hydrangea | 5’ | 4 | 20 gal
1. Camellia | 7 | 1 | 7
2. Holly | 7 | 1 | 7
3. Azalea | 4 | 4 | 16
4. Yew | 3 | 1 | 3
5. Buddleia | 6 | 1 | 6
6. Spirea | 3 | 1 | 3
7. Spirea | 3 | 1 | 3
8. Hydrangea | 4 | 4 | 16
9. Azalea | 6 | 4 | 24
10. Viburnum | 7 | 1 | 7
11. |  |  | 
12. |  |  | 
13. |  |  | 
14. |  |  | 
15. |  |  | 
Total | 50 | xxx | 92
Landscape Irrigation Needs
House
Landscape Plant Map
* 1 gallon of irrigation per foot of plant height, applied x times per month

## Slide 17: How much Rainwater can be harvested?
Draw house footprint
Divide roof into areas that go to each gutter (delineate catchments)
Measure each catchments dimensions (length & width)
Calculate catchment area for each gutter

## Slide 18
Area = Length x Width
Roof area calculations:
Example:
50’
15’
Yellow roof area
Length = 50’
Width = 15’
50 x 15 = 750 sq. ft.
Notes: You can connect rainbarrels together or simply divert excess water

## Slide 19
How much water is available
To harvest?
25’
40’
624 gallons per
1,000 square feet
0.624 gallons per
square foot
For every inch of rainfall:
>

## Slide 20
Harvesting Potential for 1 inch rain | 
Square feet of roof catchment area | 50’ * 15’ 750 ft2
Multiply by 0.624 gal/ft2 (converts ft2 to gallons per inch of rain) | 750 ft2 *0.624 gal/ft2 = 468 gallons
*Multiply by roof harvest potential (0.75 to 0.95)a | 468 * 0.75 = 351 gal 468 * 0.95 = 445 gal
Storage conversion Ex.) 55 gallon barrel | 351 / 55 = 6.4 445 / 55 = 8.1 rainbarrels
a 75% - 95% harvest potential for rooftops, Arizona Dept. of water resources data

## Slide 21
April | 1.8 inches
May | 0.55
June | 2.23
July | 3.04
August | 1.31
September | 2.15
October | 1.61
November | 2.12
Drought Year Rainfall (2007) Athens, GA
Notes: 2007 was a 150 year drought and during the growing season there was still over an inch of rain each month except May.

## Slide 22
Month | Rainfall | 624 (gal/in) |  | Volume (2007) | 
 | 2007 | 75% | 95% | 75% | 95%
April | 1.8” | 468 | 593 | 842 | 1067
May | 0.55” | 468 | 593 | 257 | 326
June | 2.23” | 468 | 593 | 1044 | 1322
July | 3.04” | 468 | 593 | 1423 | 1802
Aug | 1.31” | 468 | 593 | 613 | 777
Sept | 2.15” | 468 | 593 | 1006 | 1275
Oct | 1.61” | 468 | 593 | 753 | 954
Nov | 2.12” | 468 | 593 | 992 | 1257
Rainfall on a 20 x 50’ roof area (1,000 ft2)
Athens, GA 2007 (drought year)
a
aRain harvest potential from rooftops, Arizona Dept. of water resources

## Slide 23
55 gallons
275 gallons
- Inexpensive
Unactractive
Algae?
Time and Labor

## Slide 24
- 1200 gallons ($400+)
Opaque
Attractive

## Slide 25
Buried Tanks
- Septic tanks (baffles)
- More expensive
- $1,000/1000 gallon
Excavation required
Pump
Floatation prevention

## Slide 26: Value of Harvested Rain Water Athens-Clarke County
 | Utility Costs $ / 100 cu. ft. (748 gallons) | 1,000 ft2 $ / inch of rain | Rainfall 2007 inches | 2007 $/ growing season
Water | $2.10 | $1.75 | 14.3 | $ 25.03
Sewer | $1.82 | $1.52 | 14.3 | $ 21.74
Total | $3.92 | $3.27 | 14.3 | $ 46.77
~ 10 year return on a system that costs $500

## Slide 27
Condensate from Air Conditioners and Dehumidifiers
Home AC can produce over 5 gal./day

## Slide 28
Condensate Harvesting Potential | 
AC production | Example: 7 gpd
Multiply by 7 to convert to gallons per week | 49 gal. per week
Multiply by 4 to convert to gallons per month | ~200 gal. per month
Need ~7 gal/day to get 200 gal/month
Condensate pump
-$50
-25 gal/hr
-15 feet of head

## Slide 29: Value of Harvested Condensate Athens-Clarke County, 10 gpd drip
 | Utility Cost $ / 100 cu. ft. (748 gallons) | Gallons/ season | 2007 $/ growing season
Water | $2.10 | 2400 | $ 6.74
Sewer | $1.82 | 2400 | $ 5.84
Total | $3.92 | 2400 | $ 12.58
< 10 year return on $100 investment

## Slide 30: Irrigating With Harvested Water
Conserve by watering individual plants
Notes: 4. PRAYER FOR RAIN. Periodic drought makes the problem even more pronounced, causing reservoir and river levels to drop and often forcing water authorities and elected officials to place restrictions or bans on outdoor water use in an effort to conserve available water supplies.

## Slide 31
Irrigation Controller

## Slide 32
GFCI

## Slide 33
NC State Cistern Pump Publication

## Slide 34
Ohm’s Law
Watts = Volts x Amperes
230 Volt, 5 Amp pump = 1150 Watts
115 Volt, 5 Amp pump = 575 Watts
24 Volt, 5 Amp pump = 120 Watts
12 Volt, 5 Amp pump = 60 Watts
Understanding Electricity

## Slide 35
Pump Relay
- 24 VAC from irrigation controller “flips switch”
Can be used to control AC or DC pumps
Can install an outlet for “plug-in” pumps

## Slide 36
Pumps
- May need intake screen
May need to divert some water back to reservoir to cool pump (prevent deadhead)
Consider pressure
  Loose 1 psi for every 2.31 feet of head
  Drip irrigation may require certain pressure (25psi)
Centrifugal
230VAC
Magneto drive
115 VAC
Piston Pump
115 VAC
Notes: Doesn’t take a big pump to deliver 50 gallons of water in an hour, once per week

## Slide 37
Pressure Switch

## Slide 38
Thermal Shutoff

## Slide 39
Float switch
- Shuts off pump when reservoir is empty
- Some pumps incorporate this feature

## Slide 40
Intake screen
Foot valve

## Slide 41
Irrigation Filter

## Slide 42
Emitters
- Many shapes and styles
Flow rate 0.5 – 10 gal./hr
Pressure compensating
(designed for ~25+ psi)

## Slide 43
- 25 plants (average height 2 feet tall)
- Total requirement: 25 x 2 = 50 gallons
Irrigation Example:
50 gph/60 min = less than 1 gallon per minute
- Plant requirement – 2 gallons each

## Slide 44
- 115 VAC
7.2 Amps
828 Watts
366 gph @ 30psi
Recirculation may
be needed
- Pressure regulator

## Slide 45
Example #1

## Slide 46
Most pumps are water cooled
Require 2+ GMP flow
2 gpm = 120 gph
May need to recirculate some water
Ex. 1.7 gpm, need ~.05gpm

## Slide 47
Volts: 115 VAC
Amps: 0.7 amps
Watts: 80.5 watts
PSI: On @ 0 psi; Off @ 60 psi
Flow: ~1 gallon per minute, or 60 gallons per hour
Small AC Pump Example

## Slide 48
60 psi cutoff
Water-level shutoff
Hose-end timer
Mechanical Shutoff

## Slide 49
Pumping with Solar Electricity
SUN

## Slide 50
Volts: 12 VDC
Amps: 1.9 amps
Watts: 22.8 Watts
PSI: On @ 20 psi; Off @ 35 psi
Flow: ~1gallons per minute, or 60 gallons per hour
DC Pump Example #1

## Slide 51
Volts: 12 VDC
Amps: 3 amps
Watts: 36 watts
PSI: On @ 20 psi; Off @ 35 psi
Flow: 3.2 gallons per minute, or 192 gallons per hour
DC Pump, Example #2

## Slide 52
Battery Operated Timers
Hose end
In-line
Multi-zone
Cutoff pump at 35psi

## Slide 53
DC Float Switch
Option #1 - Electronic
Prevents dry pumping

## Slide 54
Solar System
Design
Load
  Pump energy requirement
  Hours of pumping
Solar array size
  Load
  Available sunlight
  Size/rating of solar panel
  Losses
Battery Size
  -Load
  -Maintain reserve
  -Cloudy days
  -Temperature

## Slide 55
Example Load Calculations
Pump :12VDC, 1 gpm, 2 amp
Need 120 gallons of water once a week
Pump time:
100 gallons / 1 gpm = 120 minutes ~ 2 hrs/week
DC load:
2 amps * 2 hours = 4 amp hours per week (12 VDC)

## Slide 56
Solar Array Sizing
1. Average amp hour per day: 4 / 7 = 0.57
2. Multiply #1 * 1.2 for losses = 0.68
3. Average Sun hours per day (Atl) = 4.74
4. Divide #2 / #3 = 0.14
5. Amps of solar module = 0.24
6. Total number of modules = 1

## Slide 57
Watts = amps * volts
5 watts / 12 volts = 0.24 amps

## Slide 58
Charge Controller

## Slide 60
Battery Sizing
1. Max amp hours per day: 4
2. Continuous cloudy days 4
3. Multiply #2 * #3 = 16
4. Divide #3 / 0.8 to maintain battery reserve =
20 amp hour
5b. Multiply #4 * 1.19 to run pump in temperatures as low as 50 F = 24 AH

## Slide 61
Landscape Design
Irrigation Design
Harvest Rainwater
Harvest Condensate
Water Ban Survival Guide