## Slide 1
TMDL – Fecal coliform
Frank Henning
UGA Watershed
Extension Agent

## Slide 2
What is a TMDL
Calculation of the maximum amount of a pollutant that a water body can receive and still meet water standards set by EPD (designated use)
Includes a margin of safety
Designed to help improve
water quality
Why bother?

## Slide 3
305 (b) Report
Navigable waters
Published by EPD every
two years
List available online:
http://www.gaepd.org/Documents/305b.html

## Slide 4
303(d) List
Subset of 305(b) list
Lists waters that do not meet state water standards
Not supporting or Partially supporting designated use
Delist = change listing to supporting

## Slide 5
Fecal coliforms
Broad group of bacteria (most nonpathogenic)
Indicator for fecal matter
Correlated with pathogens (illness)
Laboratory test
Regulated by Georgia EPD

## Slide 7
Common Sources of
Fecal coliform Contamination
Ag runoff
Domestic animal waste
Urban runoff
Illicit discharges
Leaking & overflowing sewer lines
Treatment plant bypass
Failed septic systems
Wildlife

## Slide 8
Designated use standards for FC
Recreation (swimming):
100 counts/100 ml for coastal
200 counts/100 ml for other recreation waters
Drinking Supplies:
May – Oct. 200 counts/100ml
Nov. – April 1,000 counts/100ml
Maximum of 4,000 counts/100 ml
Fishing and Coastal Fishing:
same as drinking
Wild River and Scenic River:
No alteration of natural water quality

## Slide 9
For recreation, drinking and fishing waters, should water quality and sanitary studies show fecal coliform levels from non-human sources exceed 200 counts/100ml (Geometric Mean) occasionally, then the allowable geometric mean fecal coliform…
shall not exceed 300 /100 ml for lakes and reservoirs
shall not exceed 500 /100ml in free flowing freshwater streams
Wildlife Provision
(GA EPD, 2004)

## Slide 10
Fecal Geometric Means
Collected quarterly (4 GMs/year)
Each quarterly GM consists of at least 4 samples collected within a 30 day period
Samples collected at least 24 hours apart
GM = (Y1*Y2*Y3*Y4) ¼

## Slide 11
Example Geometric Means
Stream A
25, 25, 25, 925 counts/100ml
Avg. = 250
GM = 61.66
Stream B
200, 200, 200, 400 counts/100ml
Avg. = 250
GM = 237.84

## Slide 13
Sample Timing
Warm Quarters: May - July, Aug. - Oct.
(more human contact and more stringent FC standards)
Cool Quarters: Nov.- Jan., Feb. - April
(less human contact and less stringent FC standards)

## Slide 14
Target a stream
Cool (1,000)
Warm (200)
*Warm (200)
Cool (1,000)

## Slide 15
Target Sampling
Baseflow conditions – fecal bacteria levels
may increase 10 – 100X in storm flow
Talk to people with local knowledge & identify potential sources of coliforms
Collect samples from tributaries. Identify sample locations with map GPS or map (zillow.com)
Place bacteria data on a map or GIS database to identify hotspots
Repeat target sampling at hotspots

## Slide 16
Example TMDL Stream

## Slide 17
1
2
3

## Slide 18
4

## Slide 19
Trt. Plant
5
6

## Slide 20
12*
13

## Slide 21
15

## Slide 22
Idexx E. coli Sampling Equipment
Idexx Colilert 18 or 24
Quanti-tray 2000 (up to 2,419 cfu.100 ml
Sterile bottles
Pipette and pipette tips
Sterile water
Incubator
Gloves
Cost ~ $5 - $10 per sample
http://www.idexx.com/water/colilert/index.jsp

## Slide 23
Fecal Coliform counts/100ml | Estimated E. coli counts/100 ml | 
GA Standard | Georgia Data | EPA Data
200 | 145 | 126
1000 | 727 | 629
Fecal vs. E. coli
E.coli to Fecal coliform multiplier
E.coli * 1.38 (Vendrell, UGA, 2005)
E.coli * 1.59 (USEPA, 1986)

## Slide 24
Decrease source (Edu., Maintenance, Reg.)
Reduce transport/conveyance (filter/disconnect)
Increase mortality (time and distance)
Correcting Bacteria Problems

## Slide 25
Identify Bacteria Hotspots

## Slide 26
Corrective Actions

## Slide 27
Submitting Water Quality Data for use by Georgia EPD
http://www.gaepd.org/Files_PDF/techguide/wpb/SQAP-gwf_1.pdf

## Slide 29
Sampling &Quality
Assurance Plan
Who is involved
Qualifications
Describe problem
Why should listing
be changed?
How and when will
project be done
How can EPD be sure
that data is reliable?

## Slide 30
Sample Collection
Collection schedule – 16 samples
Trained sampling personnel (methods)
GIS Map of sample location
Proper containers, storage and holding time
Duplicates (1 for every 10 samples)

## Slide 31
Fecal coliform analysis
Certified Laboratory Analyst (city/county)
Accredited laboratory
Quality Assurance/Quality Control
  Chain of custody
  Record keeping
  Plus others