## Slide 1: Tree Protection During Construction and Landscaping Activities
Welcome to the Center for Urban Ag Web CT Classroom
Feel Free to press talk to check your voice connection.
Remember to print off the ISA CEU sign in sheets and return to Todd.
The Workshop will begin promptly at noon.
Remember to use the raise hand function to ask questions at the end of the lecture.

## Slide 2: Tree Protection During Construction & Landscaping Activities
Bob Westerfield UGA Extension Consumer Horticulturist
Todd Hurt Center for Urban Agriculture, Training Coordinator
Funds for this project were provided by the Urban and Community Forestry Grant Program administered by the Georgia Forestry Commission.

## Slide 3: Tree Protection
Bob Westerfield will cover:
  Tree Biology and Function
  Impact of Damage
    Physical
    Compaction
    Cut
    Fill
Todd Hurt will cover:
  Pre-Construction assessment
  Tree Protection Plans
  Assessment of damage
  Critical rooting distance
  Remediation

## Slide 4: Understanding Tree Biology
How does a tree actually grow?
What are the affects of heavy equipment to tree roots?
What about damage to the trunks and limbs of trees?

## Slide 8: What’s in a Root System?
The Most Vital part of the Plant.
As the roots go, so does the tree.
Protection and care are needed to protect them.
While they are amazingly strong, they are also vulnerable.

## Slide 9: Root Form & Function
The root cap protects the meristem, the area of cell division at the root tips
Root hairs absorb most of the water and are concentrated in the maturation zone
Roots transport water & nutrients in their vascular system
Root Tips
Notes: Root Form & Function
The end of root tip is covered with a root cap, that protects the meristem. The meristem is the area where cells divide and increase in number. These cells increase in length in the zone of elongation, pushing the root tip through openings in the soil.
The root hairs are very small, composed of only a single cell. They effectively adsorb most of the water taken up by the plant. They are concentrated in the zone of maturation. They are easily lost under adverse conditions.
The vascular system of the roots work to move water and soil nutrients from the root tips up to the stems vascular system.

## Slide 10: Is this what tree roots look like?

## Slide 11: The Real Story…..

## Slide 13: How far do roots extend?

## Slide 16: Air exchange?

## Slide 18: Alternatives…

## Slide 19: What about the trunk and branches of the Tree?
They are the support and transport system for water and food.
The feeding factory pipeline for the plant.
Potential for disease, insects or girdling if injured.

## Slide 23: Effect of broken branches.

## Slide 24: Compartmentalize damage.

## Slide 25: Losing a main trunk.

## Slide 28: Leaves

## Slide 29: Leaf Form & Function
Cuticle is waxy & holds moisture in
Chloroplasts intercept light and make plant food (Photosynthesis)
Stomata open to let oxygen out and CO2 in
Vascular system moves food & water
Leaf Cross Section
Notes: Leaf Form & Function
A cross section of a typical leaf shows all the internal cells. The upper layer of cells is the epidermis which is covered with a waxy cuticle which functions to help keep moisture inside the plant.
The parenchyma cells, both the palisade parenchyma and spongy parenchyma, contain chloroplasts that intercept light and manufacture carbohydrates (photosynthesis), the food of plants that supports all plant cells.
The stomata are found on the bottom of the leaf. They open and close to regulate air and moisture exchange. Oxygen, a by product of food production, is let out while carbon dioxide, a resource needed for food production, is let in. The release of moisture (transpiration), helps to cool the leaves.
The xylem and phloem make up the vascular system, and functions to move water and food through the plant. This vascular system in the leaves are called veins and they are visible on the upper and lower surface of the leaf.

## Slide 30: The absence of leaves…..

## Slide 31: The Value of a Tree?

## Slide 32: How do we save our trees from the gallows?

## Slide 33: Before Construction Begins
Meet with Contractor
  Determine which trees are possible to save
  Not every tree can be saved
  Determine parking and supply routes
  Concrete wash out area

## Slide 34: Before Construction Begins
Evaluate Trees on the Property
Create a tree inventory
Remove weak trees
Notes: Removal of bad trees at time of construction saves major money

## Slide 35: Tree Inventory
Cultivar Selections

## Slide 36: Tree Inventory
Physical or Environmental Damage

## Slide 37: Tree Inventory
Urban Stress

## Slide 38: Tree Inventory

## Slide 39: Tree Inventory

## Slide 40: Soil Compaction Values (Coder 1996)
Number of passes over the same area
% Compaction

## Slide 41: Soil Compaction (Coder 1996)
Soil Texture | Root-limiting % Pores normally filled with air
Sand | 24%
Fine sand | 21%
Sandy loam | 19%
Fine sandy loam | 15%
Loam | 14%
Silt loam | 17%
Clay loam | 11%
Clay | 13%
Root growth is limited by <15% porosity

## Slide 42: Cut and Fills

## Slide 43: Soil Fills (Coder 1996)
Soil Texture of Fill Soil | Root damage starts | Massive root Damage
Sand | 8 inches | 24 inches
Fine sand | 6 inches | 18 inches
Sandy loam | 4 inches | 12 inches
Fine sandy loam | 3 inches | 9 inches
Loam | 2 inches | 6 inches
Silt loam | 1 ½ inches | 4 ½ inches
Clay loam | 1 ½ inches | 4 ½ inches
Clay | 1 inch | 3 inches

## Slide 44: Soil Cuts (Coder 1996)
Soil Texture | Significant root damaging soil removals
Sand | 10 inches
Fine sand | 8.5 inches
Sandy loam | 7 inches
Fine sandy loam | 5.5 inches
Loam | 4 inches
Silt loam | 3 inches
Clay loam | 3 inches
Clay | 2 inches

## Slide 45: Setting up Tree Save Zones
DBH and Critical Rooting
Fencing Choices
Planning and Root Pruning
Minimizing Soil Compaction
Remediation and Recovery Times

## Slide 46: Determine the Critical Rooting Distance
Diameter Breast Height is the diameter of the trunk in inches at 4.5 feet from the ground.
Photo Courtesy of Colorado State Univ.

## Slide 47: Critical Rooting Distance
1.25 times the DBH in inches is the distance from the trunk in feet (radius) that must be protected.
20-30% disturbance into critical root zone is an impacted tree.
DBH
24”
30 feet

## Slide 48: Tree Save Fencing

## Slide 49: Zone must be maintained
Number of passes over the same area

## Slide 50: Spreading the Load
Human on Snowshoes: 0.5 psi
Human Male ( medium build): 8 psi
M1 Abrams tank: 15 psi
Adult horse (1250 lb): 25 psi
Passenger car: 30 psi
Wheeled ATV: 35 psi
Mountain bicycle: 40 psi
Racing bicycle: 90 psi
Weight and Ground Contact

## Slide 51: Spreading the Load
Terra Mat –US Forest Service
Logging Mat
(Photo courtesy of CarolinaMat.com)
4 inches of wood mulch

## Slide 52: Prepare the Trees for Construction Disturbance
Water as necessary to keep trees out of drought stress
Fertilize according to soil test and tree need
Prune and dead wood or limbs that will be in the way of construction activity
Root prune at edge of the protected zone to minimize tearing by construction equipment.

## Slide 53: Recovery Times and Remediation
Season of Construction
  Winter
    1 year
  Spring
    3-4 years
  Summer
    3 years
  Fall
    2 years
Air Spade

## Slide 54: Post-Construction Care
Remove any excessive mulch used for protection
Inspect for cut and fill changes
Prune out and damaged limbs
Water and fertilize as needed.

## Slide 55: Special Thanks To:
Joan Scales, Partnership Coordinator, GFC
Spence Rosenfeld, Arborguard
Sam Geer, Geer Tree Specialists
Robert Brettschneider, Geer Tree Specialists
Kim Coder, PhD. UGA Warnell School of Forest Resources
Dexter Adams, UGA Grounds

## Slide 56
Funds for this project were provided by the Urban and Community Forestry Grant Program administered by the Georgia Forestry Commission.
The U.S. Department of Agriculture (USDA) prohibits discrimination in all its programs and activities on the basis of race, color, national origin, gender, religion, age, disability, political beliefs, sexual orientation, and marital or family status. (Not all prohibited bases apply to all programs.) Persons with disabilities who require alternative means for communication of program information (Braille, large print, audiotape, etc.) should contact USDA’s TARGET Center at 202-720-2600 (voice and TDD).
To file a complaint of discrimination, write USDA, Director, Office of Civil Rights, Room 326-A, Whitten Building, 14th and Independence Avenue, SW, Washington, DC 20250-9410 or call 202-720-5964 (voice or TDD). USDA is an equal opportunity provider and employer.